## Slide 1: Lecture 4 The CMOS Inverter
Dynamic properties

## Slide 2: Week 2: The CMOS inverter
Tuesday
  Static properties
    Voltage transfer curves (VTC)
    Noise margins
  Exercise (Kjell, 1 hour)
Thursday
  Dynamic properties
    Propagation delay
    Driving large capacitive loads w. optimal propagation delay
  Exercise POTW (Victor, 2 hours)
Friday
  Prelab 1 deadline 1PM

## Slide 3: Last time? Muddy?
How switching voltage is calculated
NOR/NAND gate VTC
Noise margins
  How calculate them
  Are they accurate from simplified models?
  Where does 1/8 come from in noise margin example?
  Butterfly diagram
Cox what is that?

## Slide 4: Voltage Transfer Characteristic - VTC
. . . and saturation currents are equal:
VIN
VOUT
VDD
NMOS OFF
PMOS OFF
VDS
IDS
Saturation: IDSP,N=IDSAT,P
VSW
VSW
Inverter
IDS
VSW
VDD, VDD
Switching occurs in the green region where both MOSFETs are saturated . . .
VDD
Switching means:
VIN=VOUT
Solving for VIN using x=kN/kP yields

## Slide 5: Noise margins

## Slide 6: Noise Margins – an example
VIN
VDD
VOUT
VDD
0
0
VIL,max
VIH,min
VOH,min
Valid ”0”
Valid ”1”
Formulas can be derived (for x=1): VOH,min=VDD-DV/8 VOL,max = DV/8
VIL,max=VSW-DV/8
VIH,min=VSW+DV/8
0.28 V
0.28 V
DV=0.64 V
DV/8
DV/8
DV/8
DV/8
Formulas can be derived (for x=1):
VOH,min=VDD-DV/8=1.12 V VOL,max = DV/8=80 mV
VIL,max=VSW-DV/8=0.52 V
VIH,min=VSW+DV/8=0.68 V
For x=1, VTN=0.28 V and VTP=-0.28 V we have VSW=0.28+0.64/2=0.60 V
and DV=0.64 V
VOL,max
These points yields numbers for (VOH,min, VIL,max) and (VOL,max, VIH,min)
so that NMH and NML can be calculated!
NMH=VOH,min-VIH,min NML=VIL,max- VOL,max
NMH=VOH,min-VIH,min1.12-0.68=0.44 V NML=VIL,max- VOL,max = 0.52-0.08=0.44 V
Let´s define valid regions from points where slope AV = -1!
VDD = 1.2 V

## Slide 7: Quick question
Have you tried solving prelab 3 yet?
Notes: Take a few minuteson your own and then discuss with your neighbor.

## Slide 8: Static vs dynamic
Last time: static (DC) behavior
Input: DC voltage,
Output: DC voltage
This time: dynamic behavior
That is, with time
Input: voltage waveform
Output voltage waveform
VDD
VIN
ON
OFF
VOUT
VDD
VIN
ON
OFF
VOUT
VOUT=1.2V
VIN=0.2V
In circuit simulation: DC analysis
In circuit simulation: transient analysis
CL
Notes: The load capacitor CL a placeholder.
Some current charges and discharges the load capacitance.

## Slide 9: Outline
Definitions
  Rise time and fall time
  Propagation delay: Rise delay and fall delay
Propagation delay estimation
  Step response model
    Charging and discharging the load capacitor
  Ramp response model
    Introducing the MOSFET effective resistance
Inverter capacitances
  Model for scaled inverter: effective resistance and capactiance
Inverter pair delay
  Normalizing the inverter delay wrt t=0.7RC
Delay w. more than one inverter
  Inverter pair delay
  The fanout-of-four (FO4) delay
  The tapered buffer, finding sizes and number of inverters
  (Buffers/drivers with branching)

## Slide 10: Definitions for waveforms
VIN
Time, t
100%
tr
tf
20%
80%
0
Input signal definitions: rise and fall times
Falling edge
Rising edge

## Slide 11: Definitions for delay
VIN
Time, t
100%
tpdf
50%
0
Propagation delay definitions: rise and fall delays
VOUT
Time, t
100%
50%
0
tpdr
Propagation delays are defined at the 50% level!

## Slide 12: Step-response model
VIN
Time, t
100%
tpdf
50%
0
VOUT
Time, t
100%
50%
0
tpdr
Output fall delay
Output rise delay

## Slide 13: Step-response model
VSS
VDD
VDD/2
IDS,P
VOUT
IDSAT,P
pMOS current flow in detail
VDD
VIN
ON
OFF
VIN=LOW
VOUT
CL
1. Charging the load capacitor through the p-channel MOSFET
Output rise delay
VIN goes LOW
VOUT goes HIGH
Notes: Note that the xcharging current is constant!

## Slide 14: Step-response model
VDD
VSS
CL
VIN
VOUT
2. Discharging the load capacitor through the n-channel MOSFET
OFF
ON
VIN=HIGH
Output fall delay
VDD
VDD/2
IDS,N
VOUT
nMOS current flow in detail
IDSAT,N
VIN goes HIGH
VOUT goes LOW
Notes: Note that the current is constant!

## Slide 15: Step-response model accuracy
How good is the step-response model?
  Real world input voltages are not step functions
  They are output voltages from other gates

## Slide 16: Step response model accuracy
Experience and hundreds of circuit simulations show that propagation delays are about 40% longer in designs where input and output edge rates are equal
Notes: We add another 40% to match.

## Slide 17: The most important equation

## Slide 18: Ramp input – output trace
VGS rises from 0 to VDD
VIN:
VGS = 0
VGS = VDD
Some discharge happens while input rises from 0 to VDD
Most discharge still happens with IDSAT,max

## Slide 19: Effective resistances: 65 nm MOSFETs
Reff=VDD/IDSAT,max
Reff=VDD/IDSAT,max
RN,eff=2 kW.mm
RP,eff=4 kW.mm
IDSAT,max =
600 mA/mm
VDD=1.2 V
N-channel device
P-channel device
IDSAT,max =
300 mA/mm
VDD=1.2 V
IDS
VDS
IDS
VDS
VDD
VDD
Notes: Note that a wider transistor give more current, that is less effective resistance.
Note that Reff has no fixed relation to GON which depends on the threshold voltage.
SO I = Reff x Vout

## Slide 20: The most important equation revisited
Notes: About the 0.7 factor – it is annoying but we have to live with it….

## Slide 21: RC delay
VOUT
VSS
CL
VDD
Reff
This RC circuit has an output voltage delay given by

## Slide 22: Ramp input – output response
The two curve forms are not the same, but they yield the same delay!
Notes: The curves are not the same but they coincide at the important 50 % point. The effect of the ramped response is correct there. The 0.7 factor helps here.
The purple curve is slower at the beginning because current is not so large yet.

## Slide 23: MOSFET capacitances (from lecture 2)
STI
STI
L, the channel length
drain
source
LD
LS
Cbottom
Csidewall
Cbottom
Csidewall
L
Metal gate
Silicon substrate
W, the channel width
There is a distributed gate capacitance that must be lumped to to the available ckt nodes, that is, source and drain
There are parasitic capacitances from source/drain to substrate
Notes: This is where Cox can be viewed. Cox is the capacitance per area of the gate-channel

## Slide 24: 65 nm CMOS capacitances
LS
LD
W
Gate capacitance
Plate capacitance between gate and channel (but here we model it between gate and source)
CG=WLCox
Cox≈20 fF/μm2
(corresponds to 1.2 nm effective oxide thickness, tox)
60 nm effective channel length yields:
CG=1.2 fF/μm
Drain/source parasitic capacitances
Same order of magnitude as the gate capacitance, CS=CD=pinvCG
Generic approach is to use pinv=1 for simplicity
But sometimes pinv=0.5 or pinv=0.8!
channel
length, L
Notes: Minimum LD and Ls are given by design rules as we will see in week 4.

## Slide 25: Electrical model for saturated MOSFET (from lecture 2)
VG
VD
VS
VS
IDSAT
Model for saturated MOSFET
Valid for both nMOS and pMOS transistors
CD
CG
Notes: Model has been slightly updated so that it is correct also for pMOSFETs

## Slide 26: The inverter and its electrical model
Replace the MOSFETs with their equivalent electrical circuits!
VIN
VOUT
VSS
VDD
NMOS
VIN
VOUT
VSS
CGN
CDN
VSS
IDSN
IDSN
PMOS
VDD
CGP
CDP
VDD
IDSP

## Slide 27: The inverter and its electrical model
VIN
VOUT
VSS
VDD
NMOS
VIN
VOUT
VSS
CGN
CDN
VSS
IDSN
IDSN
PMOS
VDD
CGP
CDP
VDD
ISDP
Change the sign of the pMOS current so that all currents are positive
(We also made the pMOS voltages positive, although it is not necessary)

## Slide 28: The inverter and its electrical model
Place all capacitors to signal ground! Both rails are constant voltages, no dV/dt
VIN
VOUT
VSS
VDD
VIN
VOUT
VSS
VSS
IDSN
IDSN
VDD
VDD
ISDP
CG=CGN+CGP
Inverter input capacitance: CG=CGN+CGP; MOSFET gate capacitances add!
Inverter parasitic output capacitance: CD=CDN+CDP. Drain caps also add!
CD=CDN+CDP

## Slide 29: The inverter and its electrical model
Eliminate VDD rail by inserting power supply to signal ground!
VIN
VOUT
VSS
VSS
IDSN
Inverter input capacitance: CG=CGN+CGP; MOSFET gate capacitances add!
Inverter parasitic output capacitance: CD=CDN+CDP. Drain caps also add!
VIN
VOUT
VSS
VDD
CG=CGN+CGP
CD=CDN+CDP
ISDP
VDD

## Slide 30: The inverter and its electrical model
Replace MOSFET constant-current sources with their effective resistances!
VIN
VOUT
VSS
VSS
RN,eff
Inverter input capacitance: CG=CGN+CGP; MOSFET gate capacitances add!
Inverter parasitic output capacitance: CD=CDN+CDP. Drain caps also add!
VIN
VOUT
VSS
VDD
CG=CGN+CGP
CD=CDN+CDP
RP,eff
VDD
RN,eff=2 kW.mm
RP,eff=4 kW.mm

## Slide 31: The inverter and its electrical model
Too cumbersome to have different rise and fall delays!
Replace effective resistances with one average effective resistance!
VIN
VOUT
VSS
VSS
Inverter input capacitance: CG=CGN+CGP; MOSFET gate capacitances add!
Inverter parasitic output capacitance: CD=CDN+CDP. Drain caps also add!
VIN
VOUT
VSS
VDD
CG=CGN+CGP
CD=CDN+CDP
VDD
RN,eff=2 kW.mm
RP,eff=4 kW.mm
Reff=3 kW.mm
W=1
W=1

## Slide 32: The inverter and its electrical model
Too cumbersome to have different rise and fall delays!
Replace effective resistances with one average effective resistance!
VIN
VOUT
VSS
VSS
RN,eff=2 kW.mm
Inverter input capacitance: CG=CGN+CGP; MOSFET gate capacitances add!
Inverter parasitic output capacitance: CD=CDN+CDP. Drain caps also add!
VIN
VOUT
VSS
VDD
CG=CGN+CGP
CD=CDN+CDP
VDD
Or even better!
Design the inverter for equal effective resistances, RP,eff=RN,eff, by making p-channel MOSFET twice as wide as the n-channel MOSFET to compensate for the lower hole mobility
W=2
W=1

## Slide 33: Inverter capacitances
VIN
VOUT
VSS
VDD
VIN
VOUT
VSS
VSS
CG=3.6 fF/mm
CD=pinvCG
VDD
W=2
W=1
Task: Calculate CG and CD with pMOS FET is twice as wide as nMOS FET expressed in the width of the nMOS transistor.
Answer: Assuming L=60 nm and Cox=20 fF/mm2 we obtain CGN=1.2 fF/mm and CGP=2.4 fF/mm. Hence CG=3.6 fF/mm.
Concerning CD we assume CD=pinvCG=3.6 fF/mm with pinv=1.
RN,eff=2 kW.mm
We notice that CG × RN,eff is a constant. It will soon return!
Notes: So it the total transistor width (p+n) is 1 um
Answer: Assuming L=60 nm and Cox=20 fF/mm2 we obtain CGN=1.2 fF/um and CGP=2.4 fF/um. Hence CG=3.6 fF/um.
Concerning CD we assume CD=pinvCG=3.6 fF/mm with pinv=1.

## Slide 34: More than one inverter

## Slide 35: Inverter pair delay
Reff
VDD
Task: Calculate the inverter pair delay!

## Slide 36: Inverter pair delay
CG
Reff
VDD
Put on your “two-port glasses” and look towards the loading inverter!
You will only see the input capacitance of the loading inverter

## Slide 37: Inverter pair delay
Reff
CD
VDD
CD
Have your “two-port glasses” on and look towards the driving inverter!
You will see a voltage source with a certain source resistance, and you will see the parasitic capacitance of the loading inverter

## Slide 38: Inverter pair delay
Reff
VDD
In an ideal inverter the time constant tau is really what the name says, a constant;
It is independent of inverter size (as long as WP/WN=2).
CG
CD
Propagation delay:
All delay calculations are made wrt to this technology time constant tau (𝜏)

## Slide 39: Inverter pair delay
Reff
VDD
Propagation delay:
All delay calculations are made wrt to this technology time constant tau (𝜏)
Equivalent electrical circuit for propagation delay calculations
CG
CD
VOUT

## Slide 40: Important concept
The technology time constant tau, 𝜏:

## Slide 41: Quiz time!
  Go to socrative.com
  Select Student login
  Go to room: “MCC0922018”

## Slide 42: Inverter FO4 delay
The FO4 propagation delay in our 65 nm process:
X1
X1
X1
Reff
CD
VDD
X1
X1
CG
CG
CG
CG
One inverter drives 4 identical inverters
Notes: We will motivate why this is important

## Slide 43: Normalized FO4 delay
Normalized delay means normalized to 𝜏
X1
X1
Reff
CD
VDD
X1
X1
CG
CG
CG
CG
So FO4 normalized delay:
X1

## Slide 44: Important concept
The normalized delay, d:
Where tau, 𝜏, is the technology time constant, 𝜏

## Slide 45: FO4 delay trends vs. feature size
1 mm
1/4 mm
0.13 mm
65 nm
22 nm
0.5 mm
32 nm

## Slide 46: Microprocessor cycle time trends
From Weste & Harris.

## Slide 47: Inverter Size
In most vendor cell libraries, inverters and other logic gates come in a number of different varieties concerning their driving capability (Reff) and input capacitance (CG).
In the following all inverters and logic gates of a certain size, e.g. size X=8, will have the same input capacitance, and, as an example, this input capacitance will be only half the input capacitance of a gate of size X=16.
Notes: For inverters this is not a bproblem, for other gates it can be more confusing.

## Slide 48: Minimizing delay through multiple inverters

## Slide 49: Path definitions
Reff/x1
Reff
Reff/x2
CL=HC
x1C
x2C
H is the
path electrical effort
C
Path electrical effort: H = CL/CIN
Stage electrical effort or fanout for inverter n: hn = CINn+1/CINn = xn+1/xn
Normalized delay for inverter n: dn = hn + pinv
Normalized path delay with N stages : D = N × pinv + h1 + h2 + … + hN
Notes: These concepts will come lack next Thursday.

## Slide 50: The tapered buffer with 3 stages
Reference inverter . . .
and two inserted buffer inverters
C
Normalized path delay: D = 3 pinv + h1 + h2 + h3 where h1=x1, h2=x2/x1 and h3=H/x2.
But only h1 and h2 are independent variables, h3 becomes h3=H/h1h2:
D = 3 pinv + h1 + h2+ H/h1h2
Show that minimum delay is obtained for h1=h2=3√H, which gives:
Dmin = 3 pinv + 3 × 3√H
Size x1
Size=1
Size x2
Reff/x1
Reff
Reff/x2
CL=HC
x1C
x2C
H is the
path electrical effort

## Slide 51: The tapered buffer with 3 stages
Example with path
electrical effort H=64
Reference inverter . . .
and two inserted buffer inverters
C
Normalized path delay: D = 3 pinv + h1 + h2 + h3 where h1=x1, h2=x2/x1 and h3=H/x2.
But only h1 and h2 are independent variables, h3 becomes h3=H/h1h2:
D = 3 pinv + h1 + h2+ H/h1h2
Example: H = 64
Minimum delay is obtained for h1=h2=3√64=4 gives D = 3(pinv+4)=15 with pinv=1
Size x1 = 4
Size=1
Size x2 = 16
Reff/4
Reff
Reff/16
CL=64C
4C
16C

## Slide 52: The tapered buffer with N stages
What if the path electrical effort, for some reason, is very large, e.g. H=4096.
How many inverters, N, are needed to minimize the delay?
CL=HC
C
Size=1
Large path electrical
effort H=4096=212
Minimum path delay D=N(pinv+h)? Determine best N and h!

## Slide 53: Best h & N?
Optimal h with pinv=0 can be shown analytically to be h=e= 2.72 for Nopt = ln(H)
With larger pinv numerical solution gives h≈4
  That is why the FO4 delay is so important!
The minimum is, so a bit larger h does only increase delay marginally and substancially smaller area

## Slide 54: Quick question
If you were to design a tapered buffer where the load capacitance is 1500 times larger than the input capacitance, and you are not allowed to invert the signal, how many inverters would you choose?
What would be the resulting normalized delay for the buffer?

## Slide 55: H-tree clock distribution

## Slide 56: H-tree clock distribution
What is the timing path electrical effort?
What sizes to choose for inverters in the H-tree?

## Slide 57: Short summary
The technology time constant, tau
The inverter propagation delay, with effective resistance
The normalized delay
Normalized inverter pair delay
Normalized fanout-of-four ( FO4) delay
Tapered buffer with path fanout H and N stages (D is normalized path delay)
Optimal h is around 4

## Slide 58: Long summary
Defined rise and fall delays at the 50% level (VDD/2) andrise and fall times between 20% and 80% levels
Calculated propagation delay in response to a square-wave input signal assuming MOSFETs being saturated during delay
Improved the delay model by adding 40%
  assuming a ramp input signal and
  assuming equal input and output edge rates
Replaced saturation current sources by effective resistances
Made the pMOSFET twice as wide to compensate for lower hole mobility
  Both MOSFETs now have the same effective resistance of 2 kW.mm
  However, p-channel device now has twice the input capacitance of the n-channel MOSFET
Obtained an electrical two-port model of the inverter for delay calculations
  we know what this model looks like seen from the input port, and seen from the output port
Calculated the FO4 delay, and we found the ReffCG product being independent of the inverter size (as long as we keep same ratio between WP and WN)
Introduced technology time constant, tau, and normalized delay, d
Found best inverter sizes of a tapered inverter buffer for minimum delay. Fanout h = 4 is the optimum.