## Slide 1: Layout of CMOS gates

## Slide 2: Week 4
Monday lab2
  Carry gate schematic
Tuesday
  Lecture Layout of CMOS gates
Thursday
  Prelab lab 3, Geometrical design rules
  Postlab review lab 2
  Tutorial POTW Layout (Victor)
Friday Deadline prelab 3
  Layout of carry ckt of full adder

## Slide 3: From MUD cards
Path delay optimization complicated to understand.
Did not quite get the delay optimization example.
More simple examples before a more complex one.
Still confused to find out h, p.
In D=N × fopt + P, why is P sum of all parasitic delay?
Have the slides earlier before lecture? Not always possible, but the slides from last year are there.

## Slide 4: Summary path delay optimization
Goal: minimize normalized path delay (that is, critical path delay)
Path effort F= G × H × B (general expression for all cases)
path electrical effort: H = CL/CIN (for entire path)
path branch effort: B = b1 × ….. × bN (for entire path)
path logical effort : G = g1 × …..× gN (for entire path)
Optimal stage effort is fopt = N√F
Optimal path delay Dopt is then: Dopt = N × fopt + P
where P is path parasitic delay = sum of all p in path
Read W&H section 4.5 Logical Effort of Paths

## Slide 5: Clock tree task from latest exam
Find fopt, Dopt and
the input capacitances at
stages 2 and 3
Work in small groups
Replies in socrative.com room: MCC0922018 as usual
FIXED
FIXED
SCALABLE
SCALABLE

## Slide 6: Clock tree task from latest exam
Find fopt, Dopt and
the input capacitances at
stages 2 and 3
Work in small groups
Replies in socrative.com room: MCC0922018 as usual
First steps towards
solution:
F = G × B × H
F = (32/3)^2

## Slide 7: Clock tree task from latest exam
Find fopt, Dopt and
the input capacitances at
stages 2 and 3
Work in small groups
Replies in socrative.com room: MCC0922018 as usual
Solution:
fopt = 32/3
Dopt = 38
(assuming pinv = 1)

## Slide 8: Clock tree task from latest exam
Find fopt, Dopt and
the input capacitances at
stages 2 and 3
Work in small groups
Replies in socrative.com room: MCC0922018 as usual
Solution:
fopt = 32/3
Dopt = 38
(assuming pinv = 1)
Stage 3: CIN =
(4/3)× 32C/(32/3) = 4C
Stage 2: CIN =
(4/3) × (4Cx4)/(32/3) = 2C

## Slide 9: Improve delay by adding one inverter stage – how much is path delay improved?
Find new
fopt, Dopt
with added stage
Later you can calculate the sizes too
I will post those numbers
FIXED
FIXED
SCALABLE
SCALABLE
SCALABLE

## Slide 10: Improve delay by adding one inverter stage – how much is path delay improved?
Find new
fopt, Dopt
with added stage
Later you can calculate the sizes too
I will post those numbers
Solution:
F =(32/3)^3
fopt = 4√F≈ 5.9
Dopt = 4 × 5.9 + 7pinv =
30.6 (assuming pinv = 1)

## Slide 11: Improve delay by adding one inverter stage – how much is path delay improved?
Find new
fopt, Dopt
with added stage
Later you can calculate the sizes too
I will post those numbers
Solution:
F =(32/3)^3
fopt = 4√F≈ 5.9
Dopt = 4 × 5.9 + 7pinv =
30.6 (assuming pinv = 1)
CIN2 = 5.9C
CIN3 = 6.5C
CIN4 = 7.2C

## Slide 12: Aim of lecture
To give some basic understanding of layout trade-offs between wiring and transistors
To provide guidelines for systematic and structured design using standard cell templates
To discuss the influence of layout on performance
To use Euler paths to minimize parasitics and letting MOSFETs share common source/drain areas
To introduce methods for symbolic layout on virtual grids
Notes: Why bother with physical design?

## Slide 13: The inverter - - from schematic to layout
IN
Inverter schematic
IN
VDD
VSS
OUT
Well tie
Substrate tie
VDD
VSS
OUT
Body ties
Active areas
Contacts to active areas
Poly gates
Contacts to poly gates
Metal wiring
Poly only vertically
Metal mainly horizontally
How do we get through with metal wiring?
Inverter schematic
Power supply rails

## Slide 14: The inverter - - from schematic to layout
Vertical poly straps
IN
Well tie
Substrate tie
VDD
VSS
OUT
How do we get through with metal wiring?

## Slide 15: The inverter - - from schematic to layout
Well tie
Substrate tie
VDD
VSS
How do we get through with metal wiring?
Active supply straps
IN
OUT

## Slide 16: The inverter - - from schematic to layout
Well tie
Substrate tie
VDD
VSS
How do we get through with metal wiring?
WIRES ARE SHORTED!
Areas in the same layer connect if crossing or too close!
IN
OUT

## Slide 17: Inverter mask set and fabrication
P-type silicon substrate
N-well
Active areas
P+ select
Poly gate
Contact cuts
Metal wires
Notes: From which direction do we see things?
The answers here are correct but there is a very important additional reason why a p-type substrate is preferred.
NMOS transistors are faster than PMOS transistors all else being equal. To make n channel MOS, the well must be p type. To get the maximum electron mobility, the p should be as lightly doped as practical. If an n type substrate were employed that would mean that the n channel MOS would be made with the addition of a p well. This p well would need to have a significantly higher doping than the n type substrate (each added dopant must be an order of magnitude higher than the background dopant). Now the p is higher than it needs to be for the n MOS.
Although most of the circuitry is CMOS (PMOS + NMOS gates), critical components that must run fast are exclusively NMOS. The fastest NMOS is obtained with a high resistivity p-type substrate, not a lower resistivity p-well in an n-type substrate.
The conventions came after this insight into performance.

## Slide 18: Above metal 1? A metal stack with many layers for wiring
Layers M2 and up
not used in cells.
Routed by tools.
Three types of wires:
Bottom/middle/top
Corresponds to wiring:
In cell/local/global
More about this next week!

## Slide 19: Standard cell architecture
VDD
VSS
2.6
A
B
Fixed cell height: 2.6 um
Fixed supply rails
Fixed n-well regions
Fixed contact size and positions

## Slide 20: Standard cell architecture
VDD
VSS
Fixed cell height: 2.6 um
Fixed supply rails
Fixed well
Fixed contact size and positions
But MOSFET widths can be change within limits for different inverter sizes (within limits).
For even wider inverters put transistors in parallel.
A
B
2.6
A certain number of pitches are required, plus one extra space at bottom
Pitch 1
Pitch 2
Pitch 3
Pitch 4
Extra space
How many wire tracks can fit the empty space between the MOSFET source/drain contacts?

## Slide 21: Stick Diagrams
Stick diagrams help plan layout quickly
  Need not be to scale
  Draw with color pencils or dry-erase markers

## Slide 22: Merging drain areas example NOR2 n-net
B
A
Y
Notes: I added some slides here because in my experience this is something some students find very hard to grasp.

## Slide 23: Merging drain areas example NOR2 n-net
B
A
Y
Notes: Benefit?

## Slide 24: Merging drain areas example NAND2 n-net
B
A
Y

## Slide 25: Merging drain areas example NAND2 n-net
B
A
Y
Notes: And how does it look from the side? Draw on board!

## Slide 26: The NAND2 gate
ina
inb
inb
inc
ina
ina
inb
out
VDD
VSS
out
out
NAND2
inb
inc
out
VDD
ina
VSS
The NAND3 gate
NAND3

## Slide 27: The NOR3 gate
ina
inb
inb
inc
ina
NOR2
NOR3
out
out
inb
ina
out
VDD
VSS
NOR2
inb
ina
out
VDD
VSS
inc
NOR3

## Slide 28: The AOI12 gate
ina
inb
inb
inc
ina
inc
inb
ina
out
VDD
VSS
out
AOI12
Notes: Was this really the best solution?

## Slide 29: The AO212 gate
A
B
D
E
C
B
E
Z
VDD
VSS
E
A
B
A
C
D
D
C

## Slide 30: The AO212 gate
B
E
Z
VDD
VSS
E
A
B
A
C
D
D
C
A
B
D
E
C

## Slide 31: Single line of diffusion
Goal: compact cell layout with as few extra contacts and metal-1 wires as possible.
  That is: small area
  That is: low parasitics at output and intermediate nodes.
Proxy: single line of diffusion
  That is: draw the entire p/n diffusion without “lifting the pen”
Tool: Euler path

## Slide 32: Graph theory: Euler paths
B
E
Z
VDD
VSS
E
A
B
A
C
D
D
C
X
X
X
X
VDD
Z
Z
E
A
B
D
C
VSS

## Slide 33: Euler path
Graph consists of vertices (circuit nodes) connected by edges (transistors).
Euler path traverses every edge exactly once.
An Euler path exists if:
  Exactly two or zero vertices have an odd degree.
  If two vertices have an odd degree the path starts and ends in these vertices

## Slide 34: Example Euler paths
Is it possible to layout p-net, as drawn, with a single line of diffusion?
Is with it possible to layout n-net as drawn, with a single line of diffusion?
From exam 2017-10-26

## Slide 35: Example with quiz
Draw the schematic for a static CMOS gate with the logical function:
f=(A∙B+C∙D)∙(E+F+G)
1 Can the p-net be laid out with single line of diffusion?
2 If yes, can you make the order ABCDEFG work?
3 Can the n-net be laid out with single line of diffusion?
4 If yes, can you make the order ABCDEFG work?
5 Is it possible to use single-line-of-diffusion layout for
both the n-net and the p-net at the same time?

## Slide 36: Gate Matrix Layout
Cin
Set-up
cell
a0
b0
Set-up
cell
a1
b1
Set-up
cell
a2
b2
Set-up
cell
a3
b3
VDD
G3
G0
G3
P3
P3
P2
P1
G2
G0
G1
P1
P0
Cin
VSS
Cout=G3+P3(G2+P2(G1+P1(G0+P0Cin)
P0
G1
G2
P2
g0
p0
g1
p1
g2
p2
g3
p3
4-bit ripple-carry block
cin
cout

## Slide 37: Gate Matrix Layout
Cin P1 G1 P2 G2 P3 G3 P4 G4
COUT
VDD
VSS
CIN
Our task in this example: We have been given the seemingly impossible task to layout the 4-bit ripple-carry block using the layout template given below, with the given gate order!!

## Slide 38: Gate Matrix Layout
Cin
Set-up
cell
a0
b0
Set-up
cell
a1
b1
Set-up
cell
a2
b2
Set-up
cell
a3
b3
VDD
G3
G0
G3
P3
P3
P2
P1
G2
P0
P1
G1
G0
Cin
VSS
Cout=G3+P3(G2+P2(G1+P1(G0+P0Cin)
P0
G1
G2
P2
g0
p0
g1
p1
g2
p2
g3
p3
4-bit ripple-carry block
cin
It seems impossible to pass all MOSFETs in the given order without passing some MOSFETs twice!

## Slide 39: Gate Matrix Layout
Cin
VDD
G3
G0
G3
P3
P3
P2
P1
G2
G1
P1
VSS
P0
G0
P0
Cin
G1
G2
P2
Set-up
cell
a0
b0
Set-up
cell
a1
b1
Set-up
cell
a2
b2
Set-up
cell
a3
b3
Cout=G3+P3(G2+P2(G1+P1(G0+P0Cin)
g0
p0
g1
p1
g2
p2
g3
p3
4-bit ripple-carry block
cin
However, there is a solution! MOSFET blocks can be rearranged in the schematic with same functionality.

## Slide 40: Gate Matrix Layout
Cin
VDD
G3
G0
G1
G2
G3
P3
P3
P2
P1
G2
G1
P1
VSS
P0
P0
G0
Cin
P2
Set-up
cell
a0
b0
Set-up
cell
a1
b1
Set-up
cell
a2
b2
Set-up
cell
a3
b3
Cout=G3+P3(G2+P2(G1+P1(G0+P0Cin)
g0
p0
g1
p1
g2
p2
g3
p3
4-bit ripple-carry block
cin
However, there is a solution! MOSFET blocks can be rearranged in the schematic with same functionality.

## Slide 41: Gate Matrix Layout
Cin
VDD
G3
G0
P2
G2
G3
P3
P3
G1
P1
P2
G2
G1
P1
VSS
P0
P0
G0
Cin
Set-up
cell
a0
b0
Set-up
cell
a1
b1
Set-up
cell
a2
b2
Set-up
cell
a3
b3
Cout=G3+P3(G2+P2(G1+P1(G0+P0Cin)
g0
p0
g1
p1
g2
p2
g3
p3
4-bit ripple-carry block
cin
However, there is a solution! MOSFET blocks can be rearranged in the schematic with same functionality.

## Slide 42: Gate Matrix Layout
Cin P1 G1 P2 G2 P3 G3 P4 G4
COUT
VDD
VSS
CIN
Here is the resulting layout!

## Slide 43: Gate Matrix Layout
Cin P1 G1 P2 G2 P3 G3 P4 G4
VDD
VSS
COUT
CIN
The layout again, a bit more refined!
The layout is very compact and elegant, however, only post-layout circuit simulations with node capacitances extracted from the layout will reveal the exact performance of the cell.

## Slide 44: Example Layout
Complete the layout of this cell shown in the template in 3 where the n-net has already been completed. Note that for simplicity all transistors have the same widths in the template, although that may not be optimal.
Identify the five inputs and mark them clearly in the template. Then draw the required connections for the
p-net. Merge as many p-di usion areas as possible to simplify your layout.

## Slide 45: Example layout

## Slide 46: Layout of the carry cell
A
A
B
VDD
VSS
CIN
A
B
A
B
B

## Slide 47: Layout of the carry cell

## Slide 48: Connecting to a standard cell
Standard cell input/output ports can be placed anywhere in the cell
  Router routes in higher metal layers to port
  But there can be only one connection port per signal!
Lab 3 cells should be abutted
  Cin input on the edge of one end
  Cout output on the edge of other end
  Treat A & B as if they can be connected anywhere in the cell.

## Slide 49: Design rules
We will talk about geometric design rules in more detail on Thursday, but . . .
. . . you probably need to know already now that there are intralayer rules and interlayer rules
Interlayer rules between layers
0.06
0.12
poly
W
S
Pitch=W+S
0.14
0.13
poly
0.12
0.03
0.09
Diff_con
0.03
0.09
Poly_con
0.09
0.09
Poly pitch on active=190 nm
Intralayer rules: width and spacing rules for each individual layer

## Slide 50: General rules for CMOS layout
Run supply lines for VDD and VSS along the upper and lower cell boundaries
Run a vertical poly wire for each input signal
Order the poly wires to obtain maximal connectivity between transistors through abutment of source/drain areas. Connected transistors then form transistor segments.
Place n-transistor segments close to the bottom VSS supply rail and p-transistors close to the top VDD supply rail
Wires necessary to complete the design are drawn in metal, poly, or, if necessary in diffusion (for instance when connecting segments to the supply rails).
Remember to keep internal node capacitances at a minimum!